## Slide 1
Integrated hydrogen-CCU value chains
CET Partnership – 16th October 2024
Herib Blanco, Energy Technology Analyst
Notes: I will aim to cover 3 elements during the presentation
NZE outlook for hydrogen demand and CCU by end use
A stocktake of where we stand in hydrogen deployment from a supply and demand perspective
Some of the challenges that stand on the way between the reality today and where we need to be to be aligned with an NZE trajectory

## Slide 2
Main role for hydrogen is in industry and synthetic fuels
In 2050, industry and synthetic fuels could each represent roughly a third of hydrogen demand driven by its use as a feedstock and as a fuel for shipping and aviation
Total hydrogen demand in NZE by end use and breakdown for synfuels and industry (Mtpa H2)
Total
Synfuels
Industry
Chart: 
| 2023 | 2035 | 2050
Refining | 42.9969 | 26.2375 | 9.8413
Industry | 53.6727 | 89.4412 | 135.0423
Transport | 0.059468 | 14.4856 | 76.538
Synfuels | 2.0019e-05 | 49.0049 | 146.6132
Power | 0 | 30.1766 | 44.5142
Other | 0.58458 | 6.8848 | 7.1912
Synfuels
Refining
Transport
Industry
Other
Power
Other chemicals
Ammonia
H2-DRI
Methanol
Other industries
Other I&S
Chart: 
| 2023 | 2035 | 2050
Ammonia | 33.2015 | 34.6842 | 37.3696
Methanol | 14.9646 | 16.5731 | 17.9856
H2-DRI | 0.0055849 | 4.5424 | 30.0121
Other chemicals | 0 | 1.7123 | 12.1285
Other uses in iron and steel | 0.00061058 | 1.194 | 9.7774
Other industrial uses | 20.6652 | 10.1316 | 21.9389
Methane
Fischer Tropsch
Methanol
Ammonia
Chart: 
| 2023 | 2035 | 2050
Fischer Tropsch | 2.0019e-05 | 16.5525 | 91.6806
Ammonia | 0 | 25.6181 | 44.3448
Methanol | 0 | 5.0612 | 6.8619
Methane | 0 | 1.773 | 3.7259
Notes: Starting with the hydrogen demand and the growth needed in an NZE scenario
  In 2023, hydrogen demand was about 97 Mt with nearly 60% for industrial applications mainly methanol and ammonia and 40% in refining. These are uses that provide economies of scale which can facilitate achieving low costs for the low-emissions routes, but at the same time require large amounts of capital to achieve full conversion of the sites to low-emissions
  Going forward, hydrogen demand more than quadruples in an NZE scenario by 2050 driven by new applications.
  Synthetic fuels, which is the at the core of this workshop, is the end use that has the largest growth in an NZE scenario reaching nearly a third of the hydrogen demand in 2050. Similarly, industrial uses as feedstock more than doubles to become a third of the total hydrogen demand in 2050. The remaining third is direct hydrogen use for transport applications such as heavy-duty transport and seasonal storage for power. Use for refining quickly decreases in line with an 80% reduction in oil supply that is needed in an NZE scenario.
If we look at the synthetic fuels:
  Over 60% is in the form of oil derivatives from Fischer Tropsch. This is used mainly for aviation, where it reaches 40% of the fuel mix by 2050 as we will see later in the presentation.
  30% is in the form of ammonia which is the main fuel for long-distance shipping complementing pure hydrogen and methanol
  Less than 10% is in the form of other carbon-containing carriers such as methane and methanol given that the end uses where these carriers can be used can either be electrified, are inefficient pathways or there are more cost-effective options
In industrial uses, the main emergent use is as feedstock for direct reduction of iron which is expected to be a main route for decarbonization of steel production together with carbon capture

## Slide 3
CCU for synthetic fuels is essential in a Net Zero Scenario
CCU for synthetic fuels could reach about 10% of the CO2 captured in 2050 growing to nearly 650 MtCO2/yr by 2050
CO2 captured in NZE by CO2 fate
Chart: 
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
CO2 stored | 37.3497 | 111.299 | 976.1703 | 2385.901 | 3690.6022 | 4565.0057 | 5278.7876
CO2 used | 0.048501 | 4.7824 | 46.387 | 153.7622 | 309.9203 | 497.4201 | 645.1944
CO2 stored
CO2 used
Notes: Staying with NZE, but changing the lens to CCUS, we see that the amount of CO2 captured needs to increase by more than two orders of magnitude by 2050 in an NZE scenario
In 2024, close to 50 Mt of CO2 capture is operational. By 2030, another 40 MtCO2 could come online from projects that are under construction. The total project pipeline by 2030 adds up to nearly 430 MtCO2
In 2030, however, we would need nearly 1 GtCO2 of capture to be in line with an NZE scenario, so even if the entire project pipeline materializes, which is a big if, we would not achieve even half of the NZE needs
Looking at 2050, the picture does not look much brighter. We would need to scale CO2 capture to almost 6 GtCO2. To put this into context, this is more than the current CO2 emissions of the US and Canada combined
CO2 use, which is the topic of today’s discussion would only be 10% of this total CO2 captured, but it would represent a significant amount reaching nearly 650 MtCO2. This is equivalent to the CO2 emissions of Indonesia, the fourth most populous country in the world, had in 2022, so it is a significant amount

## Slide 4
Chemical feedstock and aviation are opportunities for CCU
Synthetic methanol could represent 40% of methanol production in 2050 in NZE. Hydrogen and synthetic kerosene reach almost half of the fuel mix for aviation in 2050
Methanol production by technology in NZE
Fuel mix for aviation in NZE
Chart: 
| 2023 | 2030 | 2040 | 2050
Oil | 13188.4475 | 12933.1176 | 7886.6815 | 2951.2617
Hydrogen | 0 | 0 | 142.9617 | 1262.1014
Synthetic kerosene | 0 | 237.2273 | 2700.4221 | 6122.8912
Biofuels | 2.313 | 1364.4579 | 3621.72 | 4598.8655
Others | 0.0019259 | -0.0022462 | 60.5319 | 420.4037
Synthetic methanol
Hydrogen
Synthetic kerosene
Fossil fuels with CCUS
Unabated fossil fuels
Others
Fossil fuel
Biofuels
Others
Chart: 
| 2023 | 2030 | 2040 | 2050
Unabated fossil fuels | 33.189 | 21.5985 | 10.7604 | 0.28435
Fossil fuels with CCUS | 11.2616 | 16.4985 | 18.771
Electrolysis | 0.01248 | 1.824 | 7.3939 | 14.7605
Others | 0 | 0 | 1.4792 | 3.5537
Notes: Looking at where this CO2 is being used, there are two main opportunities for CCU: chemical feedstock and aviation

## Slide 5
Reality is far from what is needed
Projects with FID have increased by nearly 4x in the last 2 years, but this only represents 4% of the entire project pipeline where 55% is at early stages of development
China
Europe
Middle East
North America
RoW
Chart: 
| 2022 |  | 2023 |  | 2024
Empty | 0 | 6.049 | 0 | 13.5273 | 0
FID | 6.049 | 0 | 13.5273 | 0 | 0
China | 0 | 4.1066 | 0 | 2.8072 | 9.5332
North America | 0 | 0.34388 | 0 | 0.11652 | 1.0647
Europe | 0 | 0.48823 | 0 | 2.1017 | 4.925
Middle East | 0 | 2.52 | 0 | 0 | 2.52
RoW | 0 | 0.019542 | 0 | 1.5421 | 2.0519

Line1 | 6.049 | 6.049
Line2 | 13.5273 | 13.5273
Line3 | 13.5273 | 13.5273
Line4 | 20.0948 | 20.0948
Electrolyser capacity in FID
FID/Under construction
Notes: Now, let’s transition to taking stock of where we are regarding supply and demand of hydrogen and let’s look more closely at projects that have reached FID.
At the time we published the GHR 2022, there were just 6 GW of electrolyser capacity that had taken FID.
[CLICK]
In the 12 months that lead to the publication of GHR 2023, 7 GW of additional capacity reached FID, boosted mostly by developments in China and a significant contribution from the Neom Green Hydrogen Project in Saudi Arabia, the world’s largest project that has reached financial closure so far.
[CLICK]
In the last year, another 6.5 GW of electrolysis capacity reached FID.
China strengthened its leadership, accounting for 40% of this capacity, followed by Europe, which quadrupled FIDs compared with the previous year. India has also emerged among the key players thanks to a single FID of 1.3 GW, the second-largest electrolyser project in the world having reached financial closure.
In total, electrolyser capacity that has reached FID now stands at 20 GW globally, which could result in 1.9 Mt of low-emissions hydrogen production.
China account today for around 50% of global electrolysis capacity that reached FID, building on its expertise in mass manufacturing clean energy technologies. The country is today home to 60% of global electrolyser manufacturing capacity.
China’s continued expansion of manufacturing projects is expected to drive down electrolyser costs, as we have seen before with solar PV and batteries.
Chinese manufacturers are building on the experience gained from mass manufacturing these technologies: several large manufacturers of solar panels have entered the business of manufacturing electrolysers, and they account for around one-third of China’s electrolyser manufacturing capacity.
If we look at those 20 GW from projects that have reached FID or are under construction, they just represent about 4% of the total project pipeline by 2030 that stands at nearly 520 GW
40% of the project pipeline to 2030 is in the feasibility study phase and more than half, 55%, is in the stage of concept with a low likelihood of becoming reality given the project timelines needed to become operational by 2030
So in sum, there has been progress, the electrolyser capacity with FID or under construction has nearly quadrupled in the last two years, but just 4% of the total project pipeline has reached this status

## Slide 6
Reality is far from what is needed
Projects with FID have increased by nearly 4x in the last 2 years, but this only represents 4% of the entire project pipeline where 55% is at early stages of development
Chart: 
| 2022 |  | 2023 |  | 2024
Empty | 0 | 6.049 | 0 | 13.5273 | 0
FID | 6.049 | 0 | 13.5273 | 0 | 0
China | 0 | 4.1066 | 0 | 2.8072 | 9.5332
North America | 0 | 0.34388 | 0 | 0.11652 | 1.0647
Europe | 0 | 0.48823 | 0 | 2.1017 | 4.925
Middle East | 0 | 2.52 | 0 | 0 | 2.52
RoW | 0 | 0.019542 | 0 | 1.5421 | 2.0519

Line1 | 6.049 | 6.049
Line2 | 13.5273 | 13.5273
Line3 | 13.5273 | 13.5273
Line4 | 20.0948 | 20.0948
Electrolyser capacity in FID
Chart: 
| Concept | Feasibility study | FID/Under construction
figure title text | 283.796 | 210.4624 | 20.0948
Project pipeline in 2030 by status (520 GW)
FID/Under construction
Feasibility study
Concept

## Slide 7
Offtake agreements are growing, but remain mostly preliminary
Total volume offtake agreements reached 5 Mt at the end of 2023,
but the average share of firm agreements is below 30%.
Chart: Mtpa H₂-eq
| 2021 | 2022 | 2023
Industry
Chemicals | 128.7719 | 485.4544 | 465.7645
Steel | 0 | 180 | 120.557
Refining | 195 | 131.126 | 247.289
Aviation | 0.005475 | 96.5812 | 184.3706
Shipping | 0 | 237.2455 | 314.9364
Power | 0 | 198.5 | 100.036
Other/unknown | 239.4958 | 438.27 | 1076.9859
Chart: Agreed volume (Mtpa H2-eq)
| 0 | 552.18187288115246 | 552.18187288115246 | 552.18187288115246 | 1125.5968728811524 | 1125.5968728811524 | 1125.5968728811524 | 2421.6740413735592 | 2421.6740413735592 | 2421.6740413735592 | 2722.2310413735595 | 2722.2310413735595 | 2722.2310413735595 | 3020.7670557793217 | 3020.7670557793217 | 3020.7670557793217 | 3029.8959932793218 | 3029.8959932793218 | 3029.8959932793218 | 3310.8532832793217 | 3310.8532832793217 | 3310.8532832793217 | 5065.6049287563919 | 5065.6049287563919 | 5065.6049287563919 | 5065.6049287563919 | 5065.6049287563919 | 5065.6049287563919 | 5065.6049287563919
Shipping | 0.75949 | 0.75949
Refining | 0.53746 | 0.53746
Chemicals | 0.45161 | 0.45161
Steel | 0.40111 | 0.40111
Power | 0.32002 | 0.32002
Road transport | 0.16486 | 0.16486
Aviation | 0.073076 | 0.073076
Other industries/unknown sector | 0.01 | 0.01
Power
Chemicals
Refining
Steel
Other
Aviation
Shipping
Offtake agreements signed, 2020-23
1
2
3
4
5
6
Shipping
Refining
Chemicals
Steel
Power
Aviation
Other
Notes: On the positive side we can see that policies that are already implemented are triggering action in industry, with a growing number of offtake agreements signed and the launch of several tenders to purchase low-emissions hydrogen.
[CLICK]
Offtake agreements have grown from nearly zero in 2020 to around 2.5 million tonnes in 2023.
At the end of 2023 a total of more than 5 Mt of hydrogen have been agreed in offtake deals on aggregate.
[CLICK]
When looking in more detail at these deals, we can see that the largest share of agreements was related to hydrogen trade projects without a disclosed final application.
However, all these agreements are still at the preliminary stage and are not firm agreements.
The next largest share belongs to existing applications of hydrogen today (namely refining and the chemical sectors), and since 2022 we are starting to see also offtake agreements in new applications that are getting closer to commercialisation, such as shipping or steel making.
[CLICK]
However, not all of these offtake agreements are done deals. Actually, the average share of firm agreements is below 30%, but significant differences exist between sectors.
Shipping presents the largest share of firm agreements (although the total agreed volume is still small), followed by refineries and the chemical industry, with a share of firm agreements slightly lower, but the quantities covered by the agreements being much larger.
This suggests that these three sectors are better placed to absorb large amounts of low-emissions hydrogen in the near future.
Other sectors with a significant number of offtake agreements are steel and electricity generation, although agreements in these sectors are less firm and also more regionally concentrated, with Europe accounting for almost all deals in steel production and Japan and Korea for almost all the deals in power generation.

## Slide 8
Synthetic fuels production is growing driven by China
Production has grown by nearly two thirds since 2019, with nearly 70% of growth coming from China. Realising the full project pipeline would require an annual growth nearly six times as large
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024e
Europe | 1.572 | 1.7513 | 1.8783 | 2.579 | 3.3256 | 7.2775
US & Canada | 245.5972 | 258.8056 | 272.0016 | 272.0016 | 272.0016 | 272.6315
China | 6.2988 | 6.3942 | 9.6072 | 33.7208 | 54.7169 | 119.6107
RoW | 3.3897 | 3.3897 | 3.4334 | 4.0763 | 4.6756 | 26.4882
Europe
China
North America
RoW
Chart: Mtpa H2-eq
| By product | By region | By status
Ammonia | 17.1703
Synthetic methanol | 0.99292
Synthetic methane | 0.2231
Fischer-Tropsch fuels | 1.7813
0
Europe | 2.2984
US & Canada | 5.4886
Latin America | 2.2646
Australia and New Zealand | 5.3954
RoW | 4.7206


Ammonia
North America
Europe
Latin America
FID/Operational
Feasibility
Australia
Synthetic fuel production, 2019-2024e
Announced synthetic fuel projects by 2030
Notes: Total production of hydrogen-based fuels and feedstocks is expected to grow by almost 15% in 2024, to reach a total of over 0.4 million tonnes of hydrogen equivalent per year (Mtpa H2-eq), on the basis of announced projects that have at least reached FID. This volume represents 70% of the total low emissions hydrogen production by 2023
Almost all of the year-on-year growth comes from ammonia production projects. Almost three-quarters of the new ammonia capacity that is expected to be commissioned during 2024 is located in China, 20% in the Middle East, and most of the remainder in Europe. Over half of the capacity located in China comes from just two projects in Inner Mongolia
Methanation capacity has remained nearly stable, with the biggest project to have advanced beyond demonstration stage being the Great Plain Synfuels plant with a capacity of 125 ktpa H2 – representing 99% of methanation capacity operating today
[CLICK]
The outlook for hydrogen-based fuels or feedstock based on announced projects adds up to nearly 20 Mtpa of low-emissions hydrogen production by 2030
However, only 7% has taken FID, is under construction, or is operational (13% if excluding projects at very early stages of development)
Nearly 85% of the project pipeline has ammonia as a targeted product. If all the announced capacity comes to fruition, it would be equivalent to 50% of current global ammonia production
The number of projects targeting the production of synthetic methanol, as a feedstock or fuel, is much lower, equivalent to 5 Mtpa of methanol by 2030, or almost 4% of global methanol production today
All the announced projects for Fischer-Tropsch (FT) fuel production could produce 1.8 Mtpa H2-eq. by the end of the decade, equal to 1.6% of the aviation sector jet fuel demand in 2023
[CLICK]
Projects for hydrogen-based fuels and feedstocks are widely distributed across the world, with North America and Australia having 25% each, and Europe and Latin America each with around 11% of 2030 announced output
[CLICK]
Half of the project pipeline is in the concept stage and more than 40% in the feasibility stage

## Slide 9
Cost gap is a key challenge to overcome
Hydrogen derivatives are 1.5-6 times more expensive than the fossil fuel reference. Costs are expected to come down with deployment, but a cost gap might remain for some applications
Cost differential between hydrogen derivatives and fossil-based alternatives for China in NZE
Ammonia
Methanol
Kerosene
Chart: 
| 2030
Renewable | 851.8519 | 555.7003
Fossil | 533.4313
Chart: 
| 2030
Renewable | 2671.0135 | 952.8612
Fossil | 536.0361
Chart: 
| 2030
Renewable | 416.2697 | 260.9142
Fossil | 75
USD/t
USD/t
USD/bbl
Renewable
Fossil
Notes: I have already mentioned, the demand side with the low volume of offtake agreements and the low FID share with respect to the project pipeline for hydrogen and synthetic fuels, so I want to finish with the other key challenge for synthetic fuels, the cost gap with their fossil counterparts
Even in a low-cost region such as China, the cost gap will remain in the short term
In Europe, which has higher energy prices, the cost differential is even larger
In the US, the fossil reference is lower so the gap remains